# REPUBLIC OF MAURITIUS

## Ministry of Public Infrastructure, Land Transport and Shipping

4th Floor, New Government Centre

#### PORT-LOUIS

###### MERCHANT SHIPPING NOTICE No 7 of 2001

Title: Colour Code of Gas Cylinders

Notice to Owners, Managers, Agents, Masters and Chief Engineers of Fishing vessels

Owners, Managers, Agents, Masters and Chief Engineers are informed that with implementation of   “Safety of Fishing Vessel Regulations 2000”  viz: reg 14/1 fourth schedule, gas cylinders used on ships should be marked and colour coded. Each cylinder should be clearly marked with the name of the gas and its chemical formula or symbol. The cylinder body should be coloured according to contents, with, where necessary, a secondary colour band painted around the neck of the cylinder to denote the particular hazards of the gas (flammability, toxicity, ). Examples of such colour coding on gas cylinders to be used on board ships are as follows:

| Name of Gas | Chemical formula or Symbol | Colour of Container | Colour of Band |
| --- | --- | --- | --- |
| Oxygen | O2 | Black | None |
| Carbon Dioxide | CO2 | Black | None |
| Compressed Air | None | French Grey | None |
| Nitrogen | N2 | French Grey | Grey Black |
| Acetylene | C2H2 | Maroon | None |
| Propane | None | Signal Red | None |
| Butane | None | None Specified | Signal Red |

Cylinders of refrigerant gases are not allocated specified ground or band colours.

Director of Shipping

Ministry of  Public Infrastructure, Land Transport and Shipping

4th Floor New Government Centre

Port-Louis

Republic of Mauritius.